## Slide 1: Approximate Computing
Marvin Sevilla

## Slide 2: Overview
What is Approximate Computing
Real Life Examples
Practical Applications
Under The Hood
Image Algorithm Demo
Practical Coding Demo
Closing Remarks

## Slide 3: What is Approximate Computing
What is the point of approximate computing?
  To achieve a satisfactory computational result with reliable and controllable error thresholds, in other words: relaxed precision. Basically, as Jie Han form the University of Alberta puts it, "...[it] employs active design methodologies that exploit the nature that many systems and applications can tolerate some loss of accuracy in the computation result."
Where does approximate computing help?
  Approximate computing covers things from programming language all the way down to circuit design and transistor/logic-gate scrutiny. It helps improve energy efficiency while maintaining a satisfactory level of computational accuracy.
Where might approximate computing be beneficial?
  Definitely in computing clusters used for deep learning or LLMs. The amount of heat generated from those clusters is enormous and requires a ton of power to keep cool. Reducing the amount of energy needed to power the clusters and cool them would mean money saved, cheaper and smaller hardware, and more computational efficiency per unit of space in such a facility.

## Slide 4: What is Approximate Computing
How does approximate computing get all of this done?
  Voltage Scaling + Dynamic Voltage and Frequency Scaling (DVFS). This means reducing the operating voltage of the processor. The technique even goes as far as to adjust the voltage dynamically based on the input/workload.
  Error Resilient Algorithms
    Algorithms such as the Newton-Raphson method, lossy compression (like JPEG), sorting algorithms like TeraSort (which highly performant but slightly imprecise),
  Application Approximation
    This means instead of approximating the entirety of an application, we approximate only parts of it while leaving other parts of it with higher levels of accuracy
  Quality-Aware Programming
    A programming tactic which requires that software developers be keenly aware and constantly attempting to reduce the space complexity of a program as much as possible.
  If the relaxed version of a program is different to the original, when will they converge? When can they be related again?
    There are synchronization points where the 2 converge, and often times those
    We bring the assertion or result to a previous (or sometimes future) synchronization point and verify it there
    Verification reuses existing reasoning from the original program
    Languages such as Coq analyze raw source code using user-given inference rules to validate logic

## Slide 5: What is Approximate Computing
Techniques for computationally faster algorithms that use less energy, yielding inexpensive results of lower quality with negligible error
Levels of Approximate Computing
  Logic & Circuit
  Microarchitecture (atomic functions)
  Algorithms
  Parameters
Is undeniably faster and lower-power as it is unreliable

## Slide 6: What is Approximate Computing
Classes of Approximate Computing Techniques
  Error Occurrence
    Either non-deterministic (errors happen randomly) or deterministic (achieve same every time)
  Degradation
    Concerned with error rates and outcomes
    Error rates refer to toggle-able or gradual degradation
    Error outcomes refer to
      Bounded (Toggleable)
      Catastrophic (Togglable and Gradual)
      Graceful (Gradual)
  Level
    Transistor, logic, or algorithmic
  Evaluation
    Atomic or Application

## Slide 7: What is Approximate Computing
The success of an approximated application is its reliability
Reliability looks like executing the process multiple times, and the end-state of the relaxed version matches the original version a specified number of times, we deem the program reliable to that point

## Slide 8: What is Approximate Computing

## Slide 9: What is Approximate Computing

## Slide 10: Real Life Examples
Often used to meet project budget or time requirements
Well known approximation methods include fixed point, block floating point, and floating point
"...approximate computing techniques need to exploit the error-tolerance of humans and neural networks. This optimization can lead to lightweight neural networks." (21, Srivastava, Srishti, et al. "A Survey of Deep Learning Techniques for Vehicle Detection from UAV Images." CSE Department, IIT Dharwad, India, ECE Department, NIT Trichy, India, ECE Department, IIT Roorkee, India, 2024.)
Stochiastic/Probabilistic Computing, which is designed to infer based on data (e.g. a person buys yoga pants, a set of dumbbells, books on nutrition: make an inference). Requires testing many scenarios and noting features that are freqently present in all scenarios

## Slide 11: Real Life Examples
Video Compression
Image Compression
Max Pooling
ANSYS Mesh Density
Function Approximation
Single vs. Double Precision GPU computation with Roofline Graph

## Slide 12: Real Life Examples

## Slide 13: Real Life Examples

## Slide 14: Real Life Examples

## Slide 15: Real Life Examples

## Slide 16: Practical Applications
Code Perforation, Function Substitution, Approximate Memoiztation, Relaxed Synchronization (Lock Elision), Approximate Hardware
For example, choosing between using single and half precision numbers is a difference of ~3 bytes/13 bits
In unreliable hardware such as: an ALU that concludes 2+2 = 6 or Secondary Memory that interprets the memory location 0x3452 (12 in decimal) but retrieves from decimal memory location 40

## Slide 17: Practical Applications

## Slide 18: Practical Applications

## Slide 19: Under The Hood
General Steps
  Achieve minimal error result
  Establish safe execution envelope
  Relax semantics of program
  Verify program result
Uses assertions (e.g. a / b such that b ≠ 0, where b≠0 is the assertion)
Prominent concerns with radically inaccurate results, rarely correct results, crashes or other malicious actions
These concerns are avoided via error bounding

## Slide 20: Under The Hood
First thing’s first: develop quantitative verification systems
  E.g. functions that verify the reliability of values or operations

## Slide 21: Under The Hood
Error Resilience Domains are application environments where approximate results are acceptable
  Human Perception (e.g. things we can’t hear)
  Data Redundancy (e.g. noisy data)
  Generally, areas that have “No Golden Result”
End performance can be measured via things like data processing and feature extraction
Data processing refers to the quality of filtering, compression, or equivalent action which can be measured by human perception
Feature extraction refers to the identification of properties or characteristics of a data instance using algorithms/methods

## Slide 22: Under The Hood
Quantified Reliability
  .99 * R(x,y,src,dest) <= rd(val) * op(*.) * R(val)
  In English:
    Specified Bound * Reliability of Operation <= the probability we read the value right * the probability the operand performs right * the probability that the input value itself is right
Then, we evaluate the reliability of everything (e.g. reading, writing, arithmetic, the representation of values themselves
It’s important that we use reliable inputs (determined by a function that measures their reliability), because if we put junk in, we get junk out

## Slide 23: Under The Hood

## Slide 24: Under The Hood
Ultimately,
  Probability operations must stay within the established acceptable error threshold
  Computations must still meet reliability requirements (though tolerant of errors) which can be ensured using error detection and correction mechanisms or algorithmic adjustments that compensate for potential errors
  Error-tolerant software must be tested, validated, or verified at an appropriate frequency to ensure reliable results despite the uncertainties introduced by the computer’s hardware or lower-level processes

## Slide 25: Image Algorithm Demo

## Slide 26: Practical Coding Demo

## Slide 27: Closing Remarks